Car Operating Systems
Ryan Benesky

---
The Beginning of Car Computers
- 1970s Was the beginning of the EPA and regulations to clean up the environment.
- In the late 1970s car manufactures were under pressure to increase fuel mileage and decrease pollution by the California Clean Air Act.
- Manufactures moved towards Fuel injection based systems which require computers to control the system. Virtually all cars by the 1980s where fuel injected.

---
Electronic Control Unit (ECU)
- An ECU is an embedded system that controls/monitors systems in a car.
- Combination of ECUs is known as the cars computer.
- The cars “computer” is not one system but a large number of small subsystems connected together by a network.
- Modern vehicles have up to 75+ ECUs.

---
Typical ECUs
- Engine Control Module (ECM) – Determine parameters for an Internal combustion engine.
- Electronic Stability Control (ESC) – Improves vehicle safety by preventing loss of control.
- Anti-Lock Braking System (ABS) – Improves safety by preventing the brakes from locking.

---
The Engine Control Module ECM

---
Electronic Control Module
- Controls the parameters of an internal combustion engine.
- Has developed into a closed-loop system, feeds data back into the car to make decisions
- Embedded System, resources are limited.
  - Early systems entirely look-up table based.
  - Current designs are able to compute many parameters on-the-fly but there is still a few look up tables.

---
ECM Running Modes
- Open-loop : This is when the ECM is not using input data from sensors.
  - This occurs in certain circumstances where using input data would not be beneficial. Such as: when the engine is cold, or wide open throttle.
- Closed-loop: This uses post-combustion data to compute changes for pre-combustion parameters.
  - This change was implemented as the microprocessors got faster and EPA standards got tighter. Some use data from short period of time 1trip others keep track of data for months.

---
Some ECM Parameters
- Engine Load - Computed from Air Flow Rate into the engine and Intake Manifold air pressure
- Engine Speed - Reported by the Crankshaft Position Sensor
- Coolant Temperature - Reported by the engine coolant sensor, a thermistor that varies its resistance according to the engine coolant temperature
- Throttle Position - Throttle position sensor creates a voltage signal that varies in proportion to the throttle valve opening angle
- Intake Air Temperature - Measured by another thermistor located in the Mass Air Flow Sensor unit
- Battery Voltage - Battery voltage affects the speed at which the fuel injectors open and must be taken into account in computing the fuel injector pulse length, or injector open time
- Oxygen Sensor - The oxygen density in the exhaust emissions is detected and generates a control signal back to the ECU indicating the burned air/fuel ratio.

---
Sensors
The ECM uses specially designed sensors to obtain information.

---
ECM
http://www.motoiq.com/magazine_articles/articletype/articleview/articleid/1539/understanding-the-efi-process.aspx

---
Look-up Table

---
Using ECUs as Diagnostic tool
- OBD-II – standard diagnostic testing.
- Diagnostic Problem – An error occurs but where is really?
- Logging takes place in “trips,” an error may not be presented to the driver until the same error has occurred for a number of trips.

---
OBD-II Diagnostic
http://www.4x4wire.com/toyota/4Runner/tech/OBDII_ECU/

---
Controller Area Network (CAN)
Wikipedia: Controller–area network (CAN or CAN-bus) is a vehicle bus standard designed to allow microcontrollers and devices to communicate with each other within a vehicle without a host computer.
Multi-master broadcast bus
Shared medium,
Any device can broadcast as long as the line is free
If two messages broadcast simultaneously, the message with the more-dominated id will propagate to each node and overwrite the message of the less dominate id.
Bit rates of up to 1Mbit/s are possible < 40m

---
Network types.
- There is a myriad of ECUs operating in the car
- Some systems are very critical to the operation of the car including driver safety.
  - Such as the ECM, ABS, and TCM
- Other systems such as the Radio, Door Locks, etc. These are not necessary for the operation of the car and are on a slower network.

---
Experimental Security Analysis of a Modern Automobile

---
cnslab.snu.ac.kr/twiki/bin/view/Main/Research

---
Modern ECUs
- Drive-by-Wire
- Variable Control Transmissions
- Magnetic Dampers
autospeed.com.au/cms/title_Magnetic-Dampers/A_110995/article.html

---
Telematics
- In the mid 1990's car companies started attaching powerful ECU's to the car.
- Some with networking and GPS capabilities such as on-star.

---
Future Networking Infrastructure
VANET – Vehicular Ad-hoc Networks.

---
Security
- Experimental Analysis of a Modern Automobile
- By: Joint Paper between researchers at University of Washington and University of California San Diego.
- Paper highlighting what a malicious user could accomplish if they could gain access to the car networks and computers.

---
Potential Vectors
- Physical Access – A person can attach a module to the standard OBD-II port on any car.
  - Component can stay attached
  - It is also possible to flash another module from the port.
- Malicious component – A module (even the FM radio) can be replaced by one with malicious firmware.
- Network Access – Researchers identified no less than 5 networks on the test car.

---
CAN Security
- Broadcast – All packets are physically and logically sent to all ECU's.
- Denial of Service – Priority based protocol allows malicious packets to dominate the network.
- No Authentication – Packets are not authenticated, no source information is stored in CAN packets.
- Ease of Access – Variety of tools available to access components and change settings or even re-flash the component.
- Poor Network Segregation – Car critical components need to be isolated but bridging the networks is easily accomplished.

---
CAN Security

---
ECU Security
- ECU re-flashing – Car manufactures need the ability to re-flash the ECUs to perform maintenance.
  - ECUs are required to implement security features that only allow authorized personnel to re-flash the ECU
- Diagnostic Abilities – ECUs are required to report (possible too much) information about the components
- Communication Saftey – Manufactures don't follow standards that state ECUs must remain in a safe-state even if instructed to do otherwise.

---
Attack Methodology
- Packet Sniffing – CarShark was used to monitor the CAN packets while components were cycled to determine information.
- Fuzzing – CAN packets have a small valid packet range therefore randomly selecting packets can do a significant amount of damage.
- Reverse-Engineering – Components were purchased from resellers and then dumped onto a debugging platform for reverse engineering.

---
ECU Security

---
Results

---
Results Cont.

---
Conclusions
- Car Computers are here to stay.
  - Infact, with many modern cars the computers have more control then the driver.
- Plenty of new/cool work that can be done.
  - Open source ECU Projects
  - Customization
- Car Computer security is poor.
  - Today, for must users this does not pose a problem
  - As communications infrastructure increases this may pose a bigger problem
  - Major problem is the lack of standards and the lack of implementation of standards.

---
Sources/Links
- Toyota Training Series
  - http://www.autoshop101.com/autoshop15.html
- Experimental Security Analysis of a Modern Automobile
  - www.autosec.org/pubs/cars-oakland2010.pdf
- DIY EFI
  - www.diyefi.org
- Understanding OBDII Engine Systems and Fuel Mixture Control
  - http://www.4x4wire.com/toyota/4Runner/tech/OBDII_ECU/
- Recent blog by someone hacking there car (good CAN finding info)
  - http://marco.guardigli.it/2010/10/hacking-your-car.html