## Slide 1: Bitwise Operators
CS163 Fall 2018

## Slide 2: Java Bitwise Operators
Symbol | Operator
& | Bitwise AND
¦ | Bitwise OR
^ | Bitwise XOR
~ | Bitwise NOT
<< | LEFT SHIFT
>> | RIGHT SHIFT
Java has six bitwise operators:

## Slide 3: Java AND and OR
A | B | A & B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | A ¦ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
AND operator (&) OR operator (|)

## Slide 4: Java XOR and NOT
A | B | A ^ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | ~A
0 | 1
1 | 0
XOR operator (^) NOT operator (~)

## Slide 5: Binary to Decimal
Decimal | Binary | Decimal | Binary
0 | 0000b | 8 | 1000b
1 | 0001b | 9 | 1001b
2 | 0010b | 10 | 1010b
3 | 0011b | 11 | 1011b
4 | 0100b | 12 | 1100b
5 | 0101b | 13 | 1101b
6 | 0110b | 14 | 1110b
7 | 0111b | 15 | 1111b

## Slide 6: Binary to Decimal
0-9 are used for decimal numbers (base-10):
  149 = 1*102 + 4*101 + 9*100
0-1 are used for binary numbers (base-2):
  1010b = 1*23 + 0*22 + 1*21 + *20 = 8 + 2 = 10
Example:
  10111b in decimal?
  1*24 + 0*23 + 1*22 + 1*21 + 1*21 = 16 + 4 + 2 + 1 = 23
  What is 14 in binary?
  8 + 4 + 2 = 1*23 + 1*22 + 1*21 + 0*20 = 1110b

## Slide 7: Bitwise Operator Examples
4-bit numbers:
  6 & 5 = 0110b & 0101b = 0100b = 4
  6 | 5 = 0110b | 0101b = 0111b = 7
  6 ^ 5 = 0110b ^ 0101b = 0011b = 3
  ~6 = ~0110b = 1001b = 9
8-bit numbers:
  6 << 3 = 00000110b << 3 = 00110000b = 48 (6 * 8)
  48 >> 4 = 00110000b >> 4 = 00000011b = 3 (48 / 16)

## Slide 8: Masking Operations
Clearing bits:
  x = 00101001b = 41
  want to clear top 4-bits
  x = x & 00001111b = x & 15 = 00001001b = 9
Setting bits:
  x = 00101001b = 41
  want to set bottom 4-bits
  x = x | 00001111b = x | 15 = 00101111b = 47