## Slide 1
Peer Instruction #6:
LC-3 Assembly Language
(continued)
Notes: CS160 - Intro
1
CS160 - Intro
1
This is the first peer instruction session!

## Slide 2
Translate the LC-3 instruction 0xC1C0 into LC-3 assembly code:
LC-3 Instructions
JMP R7
RET
Both of the above
None of the above
Notes: CS160 - Intro
2
Answer is C), RET and JMP R7 are exactly the same.

## Slide 3
Translate ADD R0,R1,x10 from assembly code into an LC-3 instruction in hexadecimal:
LC-3 Instructions
0x1040
0x106F
0x1070
0x107F
Cannot be done!
Notes: CS160 - Intro
3
Answer is E) x10 = 16 decimal, cannot fit into 5-bits in 2’s complement format, only stores -16 to 15.

## Slide 4
Which instruction branches to Main if R0 is less than or equal to 12?
Condition Codes
BRn
BRz
BRp
BRnz
BRzp
Twelve .FILL x000C
Main LD R1,Twelve
NOT R1,R1
ADD R1,R1,1
ADD R0,R0,R1
??? Main
Notes: CS160 - Intro
4
Answer is D), Condition codes set by R0 – 12, so negative if R0 < 12 and zero if R0 == 12.

## Slide 5
What is the value in R0, and the instruction associated with the LOOP label when the program reaches the HALT command?
5, ADD R0, R0, #3
8, ADD R0, R0, #7
3, ADD R0, R0, #5
7, AND R0, R0, #7
None of the above
AND R0, R0, #0
ADD R1, R0, #2
LOOP ADD R0, R0, #3
LD R2, LOOP
ADD R2, R2, #2
ST R2, LOOP
ADD R1, R1, #-1
BRp LOOP
HALT
Notes: CS160 - Intro
5
Answer is B) ADD R0, R0, #3 is treated as both an instruction and data by the code, so ADD R2, R2, #2 instruction increments the offset to 7. R0 goes from 0 to 3 to 8

## Slide 6
What are the values in R0,R1,R2 after the code below executes? Assume the Main label is at address x3000.
LEA and LDR
x4321, x3003, x7324
x4321, x3004, x7324
x4321, x3003, x4321
x4321, x3004, x4321
None of the above
Main LD R0,Data
LEA R1,Data
LDR R2,R1,0
HALT
Data .FILL 0x4321
Notes: CS160 - Intro
6
Answer is D) LD just loads data value (x4321), LEA gets data address (x3003), LDR gets data pointed at by R1, which is data again (x4321)

## Slide 7
What is the value in R0 and R1 after the code executes from Main label?
LEA and LDR
x1133, x2244
x2244, x3355
x3355, x903F
x3355, x927F
None of the above
Array .FILL x1133
.FILL x2244
.FILL x3355
Main NOT R1,R1
LEA R2,Array
LDR R0,R2,2
LDR R1,R2,3
HALT
Notes: CS160 - Intro
7
Answer is D), offset of 2 from R2 gives Array[2], offset of 3 gives NOT R1,R1, which is x927F.

## Slide 8
What is the PC offset field in the ST instruction shown below?
PC Offsets
0b111111011
0b111111100
0b111111101
0b100000100
0b100000101
Data0 .FILL x1234
Data1 .FILL x2345
Data2 .BLKW 1
Main LD R1,Data0
LD R2, Data1
ADD R3,R2,R1
ST R3,Data2
Notes: CS160 - Intro
8
Answer is A), Data2 is -4 offset, but PC has been incremented so -5 = ~0b000000101 + 1 = 0b111111011