## Slide 1: Chapter 5
Large and Fast: Exploiting Memory Hierarchy
Modified by Phil Sharp
Additional slides from MIT open courseware
Chris Terman. 6.004 Computation Structures. Spring 2017. Massachusetts Institute of Technology:
MIT OpenCourseWare, https://ocw.mit.edu. License: Creative Commons BY-NC-SA.

## Slide 2: Status
P8
  Big but not overly hard
    Know what helper functions are available
  200 points total, graded out of 50
    Up to 150 points extra credit
  Due next Saturday
Midterm 3
  2 parts – see Teams
  Not cumulative
  Review on Thursday
    Peer instruction will cover most topics

## Slide 3: Midterm 3 Content
Cache basics
D latch and flip-flop
State machines
Boolean algebra / implementation
Full adder
Mux / decoder
Truth tables for AND, OR, NOT, XOR, NAND, NOR, Full Adder
Basic logic diagrams, outputs given inputs
LC3 registers
Binary / Hex addition / manipulation
N/P type transistors
Sequential vs Combinational logic
Technology trends
Data movement in LC3
Controller implemented with logic vs memory
Basic RTN
DRAM vs SRAM

## Slide 4: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk

## Slide 5: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
    Word “natural” size of data
  64 Bytes common
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses or
    1–hit ratio
  Then accessed data supplied from
  upper level

## Slide 6: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 7
A
B
C
Chris Terman. 6.004 Computation Structures. Spring 2017. Massachusetts Institute of Technology:
MIT OpenCourseWare, https://ocw.mit.edu. License: Creative Commons BY-NC-SA.

## Slide 8: Cache Questions
Where should data from memory be placed in a cache
  Anywhere, or a specific location?
How do we find memory data that may be in cache
  And is the cache data valid?
Which block is replaced on a cache miss
  Optimal strategy?
What happens on a write to memory
  How do we keep memory and cache in sync?

## Slide 9: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
Number of Blocks is a power of 2
How are memory addresses mapped to the cache?
  If cache is size 2n, use lowest n address bits as cache address

## Slide 10: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Are all address bits needed?
    Only higher bits not used for the cache location
    Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 11: Cache Example
Memory size 32 words, cache size 8 blocks, 1 word per block, direct mapped
Initial state
Tag size?
Cache |  |  |  |  | 
Index |  |  | Valid | Tag | Data
0 | 0 | 0 | N |  | 
0 | 0 | 1 | N |  | 
0 | 1 | 0 | N |  | 
0 | 1 | 1 | N |  | 
1 | 0 | 0 | N |  | 
1 | 0 | 1 | N |  | 
1 | 1 | 0 | N |  | 
1 | 1 | 1 | N |  | 
Memory |  |  |  |  |  |  | Memory |  |  |  |  | 
Address |  |  |  |  | Data |  | Address |  |  |  |  | Data
0 | 0 | 0 | 0 | 0 | A |  | 1 | 0 | 0 | 0 | 0 | Q
0 | 0 | 0 | 0 | 1 | B |  | 1 | 0 | 0 | 0 | 1 | R
0 | 0 | 0 | 1 | 0 | C |  | 1 | 0 | 0 | 1 | 0 | S
0 | 0 | 0 | 1 | 1 | D |  | 1 | 0 | 0 | 1 | 1 | T
0 | 0 | 1 | 0 | 0 | E |  | 1 | 0 | 1 | 0 | 0 | U
0 | 0 | 1 | 0 | 1 | F |  | 1 | 0 | 1 | 0 | 1 | V
0 | 0 | 1 | 1 | 0 | G |  | 1 | 0 | 1 | 1 | 0 | W
0 | 0 | 1 | 1 | 1 | H |  | 1 | 0 | 1 | 1 | 1 | X
0 | 1 | 0 | 0 | 0 | I |  | 1 | 1 | 0 | 0 | 0 | Y
0 | 1 | 0 | 0 | 1 | J |  | 1 | 1 | 0 | 0 | 1 | Z
0 | 1 | 0 | 1 | 0 | K |  | 1 | 1 | 0 | 1 | 0 | AA
0 | 1 | 0 | 1 | 1 | L |  | 1 | 1 | 0 | 1 | 1 | BB
0 | 1 | 1 | 0 | 0 | M |  | 1 | 1 | 1 | 0 | 0 | CC
0 | 1 | 1 | 0 | 1 | N |  | 1 | 1 | 1 | 0 | 1 | DD
0 | 1 | 1 | 1 | 0 | O |  | 1 | 1 | 1 | 1 | 0 | EE
0 | 1 | 1 | 1 | 1 | P |  | 1 | 1 | 1 | 1 | 1 | FF

## Slide 12: Cache Example
Memory Accesses |  |  |  |  |  | 
Address |  |  |  |  | Hit/ Miss | Cache Block
0 | 1 | 1 | 1 | 0 |  | 
1 | 0 | 1 | 1 | 0 |  | 
1 | 1 | 0 | 0 | 1 |  | 
1 | 1 | 1 | 1 | 0 |  | 
0 | 0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 | 1 |  | 
Cache |  |  |  |  | 
Index |  |  | Valid | Tag | Data
0 | 0 | 0 | N |  | 
0 | 0 | 1 | N |  | 
0 | 1 | 0 | N |  | 
0 | 1 | 1 | N |  | 
1 | 0 | 0 | N |  | 
1 | 0 | 1 | N |  | 
1 | 1 | 0 | N |  | 
1 | 1 | 1 | N |  | 
Memory |  |  |  |  |  |  | Memory |  |  |  |  | 
Address |  |  |  |  | Data |  | Address |  |  |  |  | Data
0 | 0 | 0 | 0 | 0 | A |  | 1 | 0 | 0 | 0 | 0 | Q
0 | 0 | 0 | 0 | 1 | B |  | 1 | 0 | 0 | 0 | 1 | R
0 | 0 | 0 | 1 | 0 | C |  | 1 | 0 | 0 | 1 | 0 | S
0 | 0 | 0 | 1 | 1 | D |  | 1 | 0 | 0 | 1 | 1 | T
0 | 0 | 1 | 0 | 0 | E |  | 1 | 0 | 1 | 0 | 0 | U
0 | 0 | 1 | 0 | 1 | F |  | 1 | 0 | 1 | 0 | 1 | V
0 | 0 | 1 | 1 | 0 | G |  | 1 | 0 | 1 | 1 | 0 | W
0 | 0 | 1 | 1 | 1 | H |  | 1 | 0 | 1 | 1 | 1 | X
0 | 1 | 0 | 0 | 0 | I |  | 1 | 1 | 0 | 0 | 0 | Y
0 | 1 | 0 | 0 | 1 | J |  | 1 | 1 | 0 | 0 | 1 | Z
0 | 1 | 0 | 1 | 0 | K |  | 1 | 1 | 0 | 1 | 0 | AA
0 | 1 | 0 | 1 | 1 | L |  | 1 | 1 | 0 | 1 | 1 | BB
0 | 1 | 1 | 0 | 0 | M |  | 1 | 1 | 1 | 0 | 0 | CC
0 | 1 | 1 | 0 | 1 | N |  | 1 | 1 | 1 | 0 | 1 | DD
0 | 1 | 1 | 1 | 0 | O |  | 1 | 1 | 1 | 1 | 0 | EE
0 | 1 | 1 | 1 | 1 | P |  | 1 | 1 | 1 | 1 | 1 | FF

## Slide 13: Byte offset
If using byte addressing with word size of 4 bytes and one word per cache line (block size of one word) lowest 2 bits of address will not be used for the cache index
  Because address changes in those bits will not effect the index location
  x86 uses byte addressing
  LC3?
For block sizes of multiple words more of the lowest address bits will be unused
  4 word / 16 byte cache blocks = 4 unused bits
  8 word / 32 byte cache blocks = 5 unused bits
  Etc.

## Slide 14: Address Subdivision
How many bytes fit in a cache line based on this offset
Why does the Tag need to be 20 bits

## Slide 15: Example: Larger Block Size
64 blocks, 16 bytes/block, 32 bit addresses
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
Address = 1200 = 0b0000’0000’0000’0000’0000’0100’1011’0000
Tag, Index, and Offset size?

## Slide 16: Explanation
Address = 1200 = 0b0000’0000’0000’0000’0000’0100’1011’0000
Byte addressing so each block covers 16 addresses
  16 addresses represented by 4 bits
Remove lower 4 bits from 0b…10010110000
  0b…1001011 = 75 = block address
Next 6 bytes are the index
  0b001011 = 11 = cache block number
Remaining bits are the tag
  0b00000000000000000000001 = tag

## Slide 17
Chris Terman. 6.004 Computation Structures. Spring 2017. Massachusetts Institute of Technology:
MIT OpenCourseWare, https://ocw.mit.edu. License: Creative Commons BY-NC-SA.

## Slide 18
Chris Terman. 6.004 Computation Structures. Spring 2017. Massachusetts Institute of Technology:
MIT OpenCourseWare, https://ocw.mit.edu. License: Creative Commons BY-NC-SA.

## Slide 19
Chris Terman. 6.004 Computation Structures. Spring 2017. Massachusetts Institute of Technology:
MIT OpenCourseWare, https://ocw.mit.edu. License: Creative Commons BY-NC-SA.

## Slide 20: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 21: Associative Cache Example

## Slide 22: Spectrum of Associativity
For a cache with 8 entries

## Slide 23: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Cache index = lower 2 bits of address / mod by 4
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 24: Associativity Example
2-way set associative, index = lower 1 bit / mod by 2
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative, no index block can be anywhere
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 25: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
  Increased associativity increases complexity / hit time
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 26: Set Associative Cache Organization
More Tag bits and less Index bits than Direct Mapped, Why?
More Complexity than Direct Mapped

## Slide 27: Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement
  n-way set associative
    n choices within a set
  Fully associative
    Any location
Higher associativity reduces miss rate
  Increases complexity, cost, and access time

## Slide 28: Finding a Block
Hardware caches
  Reduce comparisons to reduce cost
Associativity | Location method | Tag comparisons
Direct mapped | Index | 1
n-way set associative | Set index, then search entries within the set | n
Fully associative | Search all entries | #entries
 | Full lookup table | 0

## Slide 29: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 30: Handling Writes

## Slide 31: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 32: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
  dirty: cache block holds correct data, memory has old data
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 33: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block, then update cache and memory
  Write around: don’t fetch the block, just update memory
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block, then update block in cache

## Slide 34: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 35: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 36: Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
  Extra penalty = 500 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 37: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 38: Interactions with Software
Misses depend on memory access patterns
  Algorithm behavior
  Compiler optimization for memory access

## Slide 39: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 40: Cache Design Trade-offs
Design change | Effect on miss rate | Negative performance effect
Increase cache size | Decrease capacity misses | May increase access time
Increase associativity | Decrease conflict misses | May increase access time
Increase block size | Decrease compulsory misses | Increases miss penalty. For very large block size, may increase miss rate due to pollution.

## Slide 41: Concluding Remarks
Fast memories are small, large memories are slow
  We really want fast, large memories 
  Caching gives this illusion 
Principle of locality
  Programs use a small part of their memory space frequently
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for multiprocessors
§5.16 Concluding Remarks