## Slide 1: Chapter 5 The LC-3

## Slide 2: Instruction Set Architecture
ISA = All of the programmer-visible components and operations of the computer
  memory organization
    address space -- how may locations can be addressed?
    addressibility -- how many bits per location?
  register set
    how many? what size? how are they used?
  instruction set
    opcodes
    data types
    addressing modes
ISA provides all information needed for someone that wants to write a program in machine language (or translate from a high-level language to machine language).

## Slide 3: LC-3 Overview: Memory and Registers
Memory
  address space: 216 locations (16-bit addresses)
  addressability: 16 bits
Registers
  temporary storage, accessed in a single machine cycle
    accessing memory generally takes longer than a single cycle
  eight general-purpose registers: R0 - R7
    each 16 bits wide
    how many bits to uniquely identify a register?
  other registers
    not directly addressable, but used by (and affected by) instructions
      PC (program counter)
      CC (condition codes)
      IR (instruction register)
      MAR (memory address register)
      MDR (memory data register)

## Slide 4: Instruction Processing: FETCH
Load next instruction (at address stored in PC) from memory into Instruction Register (IR).
  Copy contents of PC into MAR.
  Send “read” signal to memory.
  Copy contents of MDR into IR.
Then increment PC, so that it points to the next instruction in sequence.
  PC becomes PC+1.
EA
OP
EX
S
F
D

## Slide 5: LC-3 Overview: Instruction Set
Opcodes
  15 opcodes
  Operate instructions: ADD, AND, NOT
  Data movement instructions: LD, LDI, LDR, LEA, ST, STR, STI
  Control instructions: BR, JSR/JSRR, JMP, RTI, TRAP
  some opcodes set/clear condition codes, based on result:
    N = negative, Z = zero, P = positive (> 0)
Data Types
  16-bit 2’s complement integer
Addressing Modes
  How is the location of an operand specified?
  non-memory addresses: immediate, register
  memory addresses: PC-relative, indirect, base+offset

## Slide 6: Operate Instructions
Only three operations: ADD, AND, NOT
  Other operations can be built from these primitives
Source and destination operands are registers
  These instructions do not reference memory.
  ADD and AND can use “immediate” mode, where one operand is hard-wired into the instruction.

## Slide 7: Dataflow diagrams
Diagrams illustrate when and where data moves to accomplish the desired operation
Components in data flow diagrams:
  Registers: each register can hold 16 bits in LC-3. Several
  Register File: contains eight 16-bit registers
  ALU: combinational (no storage). Two inputs, one output, functionality can be selected.
  SEXT: combinational. Sign extension from 5 to 16 bits.
  Memory: 216 words. Addressed by 16 bit MAR and MDR holds data
How components are implemented?
  Last third of the class

## Slide 8: NOT (Register)
Note: Src and Dst could be the same register.
Assembly Ex:
NOT R3, R2

## Slide 9: ADD/AND (Register)
this zero means “register mode”
Assembly Ex:
Add R3, R1, R3

## Slide 10: ADD/AND (Immediate)
Note: Immediate field is sign-extended.
this one means “immediate mode”
Assembly Ex:
Add R3, R3, #1
Notes: .

## Slide 11: Using Operate Instructions
With only ADD, AND, NOT…
  How do we subtract?
  How do we OR? Hint: Demorgan’s law
  How do we copy from one register to another?
  How do we initialize a register to zero?
Notes: Subtract: R3 = R1 - R2
Take 2’s complement of R2, then add to R1.
(1) R2 = NOT(R2)
(2) R2 = R2 + 1
(3) R3 = R1 + R2
OR: R3 = R1 OR R2
Use DeMorgan’s Law -- invert R1 and R2, AND, then invert result.
(1) R1 = NOT(R1)
(2) R2 = NOT(R2)
(3) R3 = R1 AND R2
(4) R3 = NOT(R3)
Register-to-register copy: R3 = R2
R3 = R2 + 0 (Add-immediate)
Initialize to zero: R1 = 0
R1 = R1 AND 0 (And-immediate)

## Slide 12: Data Movement Instructions
Load -- read data from memory to register
  LD: PC-relative mode
  LDR: base+offset mode
  LDI: indirect mode
Store -- write data from register to memory
  ST: PC-relative mode
  STR: base+offset mode
  STI: indirect mode
Load effective address -- compute address, save in register
  LEA: immediate mode
  does not access memory

## Slide 13: PC-Relative Addressing Mode
Want to specify address directly in the instruction
  But an address is 16 bits, and so is an instruction!
  After subtracting 4 bits for opcode and 3 bits for register, we have 9 bits available for address.
Solution:
  Use the 9 bits as a signed offset from the current PC.
9 bits:
Can form any address X, such that:
Remember that PC is incremented as part of the FETCH phase;
This is done before the EVALUATE ADDRESS stage.

## Slide 14: LD (PC-Relative)
Assembly Ex:
LD R1, Label1

## Slide 15: ST (PC-Relative)
Assembly Ex:
ST R1, Label2

## Slide 16: Indirect Addressing Mode
With PC-relative mode, can only address data within 256 words of the instruction.
  What about the rest of memory?
Solution #1:
  Read address from memory location, then load/store to that address.
First address is generated from PC and IR (just like PC-relative addressing), then content of that address is used as target for load/store.

## Slide 17: LDI (Indirect)
Assembly Ex:
LDI R4, Adr

## Slide 18: STI (Indirect)
Assembly Ex:
STI R4, Adr

## Slide 19: Base + Offset Addressing Mode
With PC-relative mode, can only address data within 256 words of the instruction.
  What about the rest of memory?
Solution #2:
  Use a register to generate a full 16-bit address.
4 bits for opcode, 3 for src/dest register, 3 bits for base register -- remaining 6 bits are used as a signed offset.
  Offset is sign-extended before adding to base register.

## Slide 20: LDR (Base+Offset)
Assembly Ex:
LDR R4, R1, #1

## Slide 21: STR (Base+Offset)
Assembly Ex:
STR R4, R1, #1

## Slide 22: Load Effective Address
Computes address like PC-relative (PC plus signed offset) and stores the result into a register.
Note: The address is stored in the register, not the contents of the memory location.
Works like the & (address of operator) in C
LEA R1, Begin
LDR R3, R1, #0
We can use the destination register as a pointer

## Slide 23: LEA (Immediate)
Assembly Ex:
LEA R1, Lab1

## Slide 24: Example (with RTL)
Address | Instruction | Comments
x30F6 | 1 1 1 0 0 0 1 1 1 1 1 1 1 1 0 1 | R1  PC – 3 = x30F4
x30F7 | 0 0 0 1 0 1 0 0 0 1 1 0 1 1 1 0 | R2  R1 + 14 = x3102
x30F8 | 0 0 1 1 0 1 0 1 1 1 1 1 1 0 1 1 | M[PC - 5]  R2 M[x30F4]  x3102
x30F9 | 0 1 0 1 0 1 0 0 1 0 1 0 0 0 0 0 | R2  0
x30FA | 0 0 0 1 0 1 0 0 1 0 1 0 0 1 0 1 | R2  R2 + 5 = 5
x30FB | 0 1 1 1 0 1 0 0 0 1 0 0 1 1 1 0 | M[R1+14]  R2 M[x3102]  5
x30FC | 1 0 1 0 0 1 1 1 1 1 1 1 0 1 1 1 | R3  M[M[x30F4]] R3  M[x3102] R3  5
opcode

## Slide 25: Example (in assembly)
Address | Instruction | Comments
x30F6 | 1 1 1 0 0 0 1 1 1 1 1 1 1 1 0 1 | LEA R1, Lab2
x30F7 | 0 0 0 1 0 1 0 0 0 1 1 0 1 1 1 0 | ADD R2, R1, #14
x30F8 | 0 0 1 1 0 1 0 1 1 1 1 1 1 0 1 1 | ST R2, Lab2
x30F9 | 0 1 0 1 0 1 0 0 1 0 1 0 0 0 0 0 | AND R2, R2, #0
x30FA | 0 0 0 1 0 1 0 0 1 0 1 0 0 1 0 1 | ADD R2, R2, #5
x30FB | 0 1 1 1 0 1 0 0 0 1 0 0 1 1 1 0 | LDR R2, R1, #14
x30FC | 1 0 1 0 0 1 1 1 1 1 1 1 0 1 1 1 | LDI R2, Lab2
opcode

## Slide 26: LC3 Addressing Modes: Comparison
Instruction | Example | Destination | Source
NOT | NOT R2, R1 | R2 | R1
ADD / AND (imm) | ADD R3, R2, #7 | R3 | R2, #7
ADD / AND (reg) | ADD R3, R2, R1 | R3 | R2, R1
LD | LD R4, LABEL | R4 | M[LABEL]
ST | ST R4, LABEL | M[LABEL] | R4
LDI | LDI R4, LABEL | R4 | M[M[LABEL]]
STI | STI R4, LABEL | M[M[LABEL]] | R4
LDR | LDR R4, R2, #−5 | R4 | M[R2 − 5]
STR | STR R4, R2, #5 | M[R2 + 5] | R4
LEA | LEA R4, LABEL | R4 | address of LABEL

## Slide 27: Control Instructions
Used to alter the sequence of instructions (by changing the Program Counter)
Conditional Branch
  branch is taken if a specified condition is true
    signed offset is added to PC to yield new PC
  else, the branch is not taken
    PC is not changed, points to the next sequential instruction
Unconditional Branch (or Jump)
  always changes the PC
TRAP
  changes PC to the address of an OS “service routine”
  routine will return control to the next instruction (after TRAP)

## Slide 28: Condition Codes
LC-3 has three condition code registers: N -- negative Z -- zero P -- positive (greater than zero)
Set by any instruction that writes a value to a register (ADD, AND, NOT, LD, LDR, LDI, LEA)
Exactly one will be set at all times
  Based on the last instruction that altered a register
Notes: Any instructions that alters a register sets the condition code

## Slide 29: Branch Instruction
Branch specifies one or more condition codes.
If the set bit is specified, the branch is taken.
  PC-relative addressing: target address is made by adding signed offset (IR[8:0]) to current PC.
  Note: PC has already been incremented by FETCH stage.
  Note: Target must be within 256 words of BR instruction.
If the branch is not taken, the next sequential instruction is executed.

## Slide 30: BR (PC-Relative)
What happens if bits [11:9] are all zero? All one?
Notes: If all zero, no CC is tested, so branch is never taken. (See Appendix B.)
If all one, then all are tested. Since at least one of the CC bits is set to one after each operate/load instruction, then branch is always taken. (Assumes some instruction has set CC before branch instruction, otherwise undefined.)

## Slide 31: Using Branch Instructions
Compute sum of array of four integers. array starts at location x300C, program starts at location x3000.
Algorithm: (the hard part, converting to assembly is relatively simple)
pointer variable set to the of beginning of array
sum variable set to 0
counter variable set to 4
while counter not equal to 0
load first value into a temp variable
add temp variable to sum
increment pointer
decrement counter
R1  x300C R3  0 R2  4
R2=0?
R4  M[R1] R3  R3+R4 R1  R1+1
R2  R2-1
NO
YES

## Slide 32: Sum of 4 integers
;Computes sum of integers
;R1: pointer, initialized to NUMS (x300C)
;R3: sum, initially cleared, accumulated here
;R2: down counter, initially holds 4
.ORIG 0x3000
…………
DONE ST R3, SUM ;added
HALT
NUMS .FILL 3
.FILL -4
.FILL 7
.FILL 3
SUM .BLKW 1
.END
LEA R1,NUMS
AND R3,R3, #0
AND R2,R2, #0
ADD R2, R2, #4
LOOP BRz DONE
LDR R4,R1,#0
ADD R3,R3,R4
ADD R1,R1,#1
ADD R2,R2,#-1
BRnzp LOOP
R1  x300C R3  0 R2  4
R2=0?
R4  M[R1] R3  R3+R4 R1  R1+1
R2  R2-1
NO
YES

## Slide 33: Sample Program
Address | Instruction | Comments
x3000 | 1 1 1 0 0 0 1 0 0 0 0 0 1 0 1 1 | R1  x300C (PC+0x0B)
x3001 | 0 1 0 1 0 1 1 0 1 1 1 0 0 0 0 0 | R3  0
x3002 | 0 1 0 1 0 1 0 0 1 0 1 0 0 0 0 0 | R2  0
x3003 | 0 0 0 1 0 1 0 0 1 0 1 0 1 1 0 0 | R2  12
x3004 | 0 0 0 0 0 1 0 0 0 0 0 0 0 1 0 1 | If Z, goto x300A (PC+5)
x3005 | 0 1 1 0 1 0 0 0 0 1 0 0 0 0 0 0 | Load next value to R4
x3006 | 0 0 0 1 0 1 1 0 1 1 0 0 0 0 0 1 | Add to R3
x3007 | 0 0 0 1 0 0 1 0 0 1 1 0 0 0 0 1 | Increment R1 (pointer)
X3008 | 0 0 0 1 0 1 0 0 1 0 1 1 1 1 1 1 | Decrement R2 (counter)
x3009 | 0 0 0 0 1 1 1 1 1 1 1 1 1 0 1 0 | Goto x3004 (PC-6)

## Slide 34: JMP (Register)
Jump is an unconditional branch -- always taken.
  Target address is the contents of a register.
  Allows any target address.

## Slide 35: TRAP
Calls a service routine, identified by 8-bit “trap vector.”
When routine is done, PC is set to the instruction following TRAP.
(We’ll talk about how this works later.)
vector | routine
x23 | input a character from the keyboard
x21 | output a character to the monitor
x25 | halt the program

## Slide 36: Another Example
Count the occurrences of a character in an array
Program begins at location x3000
  Read character from keyboard
  Load each character from array
    Starting address of array is stored in the memory location immediately after the program
  If character equals input character, increment counter
  The end of the array is indicated by a special ASCII value: EOT (x04)
  At the end, print the number of characters and halt (assume there will be less than 10 occurrences of the character)
A special character used to indicate the end of a sequence is often called a sentinel.
  Useful when you don’t know ahead of time how many times to execute a loop.

## Slide 37: Flow Chart

## Slide 38: LC3 Assembly
; Get next character from the file
;
GETC ADD R3, R3, #1 ; Increment the pointer
LDR R1, R3, #0 ; R1 gets the next character to test
BRnzp TEST
;
; Output the count.
;
OUT LD R0, ASCII ; Load the ASCII template
ADD R0, R0, R2 ; Convert binary to ASCII
TRAP x21 ; ASCII code in R0 is displayed
TRAP x25 ; Halt machine
;
; Storage for pointer and ASCII template
;
ASCII .FILL x0030
PTR .FILL x3014
.END
.ORIG x3000
AND R2, R2, #0 ; R2 is counter, initialize to 0
LD R3, PTR ; R3 is pointer to characters
TRAP x23 ; R0 gets character input
LDR R1 ,R3, #0 ; R1 gets the next character
;
; Test character for end of file
;
TEST ADD R4, R1, #-4 ; Test for EOT
BRz OUT ; If done, prepare the output
;
; Test character for match. If a match, increment count.
;
NOT R1, R1
ADD R1, R1, R0 ; If match, R1 = xFFFF
NOT R1, R1 ; If match, R1 = x0000
BRnp GETC ; no match, do not increment
ADD R2, R2, #1
A
B
C
D
E
What instruction dereferences a pointer to load a character into a register?
2) What instruction would need to be changed if the null terminator (0) is used to signal the end of the

## Slide 39: LC3 Assembly
; Get next character from the file
;
GETC ADD R3, R3, #1 ; Increment the pointer
LDR R1, R3, #0 ; R1 gets the next character to test
BRnzp TEST
;
; Output the count.
;
OUT LD R0, ASCII ; Load the ASCII template
ADD R0, R0, R2 ; Convert binary to ASCII
TRAP x21 ; ASCII code in R0 is displayed
TRAP x25 ; Halt machine
;
; Storage for pointer and ASCII template
;
ASCII .FILL x0030
PTR .FILL x3014
.END
.ORIG x3000
AND R2, R2, #0 ; R2 is counter, initialize to 0
LD R3, PTR ; R3 is pointer to characters
TRAP x23 ; R0 gets character input
LDR R1 ,R3, #0 ; R1 gets the next character
;
; Test character for end of file
;
TEST ADD R4, R1, #-4 ; Test for EOT
BRz OUT ; If done, prepare the output
;
; Test character for match. If a match, increment count.
;
NOT R1, R1
ADD R1, R1, R0 ; If match, R1 = xFFFF
NOT R1, R1 ; If match, R1 = x0000
BRnp GETC ; no match, do not increment
ADD R2, R2, #1
A
B
C
D
E
3) What check/test could be accomplished with a NOT then an ADD of 1 then an ADD
4) What instruction loads the PC with the value found at an address in the first x100 locations of memory

## Slide 40: Program (1 of 2)
Address | Instruction | Comments
x3000 | 0 1 0 1 0 1 0 0 1 0 1 0 0 0 0 0 | R2  0 (counter)
x3001 | 0 0 1 0 0 1 1 0 0 0 0 1 0 0 0 0 | R3  M[x3102] (ptr)
x3002 | 1 1 1 1 0 0 0 0 0 0 1 0 0 0 1 1 | Input to R0 (TRAP x23)
x3003 | 0 1 1 0 0 0 1 0 1 1 0 0 0 0 0 0 | R1  M[R3]
x3004 | 0 0 0 1 1 0 0 0 0 1 1 1 1 1 0 0 | R4  R1 – 4 (EOT)
x3005 | 0 0 0 0 0 1 0 0 0 0 0 0 1 0 0 0 | If Z, goto x300E
x3006 | 1 0 0 1 0 0 1 0 0 1 1 1 1 1 1 1 | R1  NOT R1
x3007 | 0 0 0 1 0 0 1 0 0 1 1 0 0 0 0 1 | R1  R1 + 1
X3008 | 0 0 0 1 0 0 1 0 0 1 0 0 0 0 0 0 | R1  R1 + R0
x3009 | 0 0 0 0 1 0 1 0 0 0 0 0 0 0 0 1 | If N or P, goto x300B

## Slide 41: Program (2 of 2)
Address | Instruction | Comments
x300A | 0 0 0 1 0 1 0 0 1 0 1 0 0 0 0 1 | R2  R2 + 1
x300B | 0 0 0 1 0 1 1 0 1 1 1 0 0 0 0 1 | R3  R3 + 1
x300C | 0 1 1 0 0 0 1 0 1 1 0 0 0 0 0 0 | R1  M[R3]
x300D | 0 0 0 0 1 1 1 1 1 1 1 1 0 1 1 0 | Goto x3004
x300E | 0 0 1 0 0 0 0 0 0 0 0 0 0 1 0 0 | R0  M[x3013]
x300F | 0 0 0 1 0 0 0 0 0 0 0 0 0 0 1 0 | R0  R0 + R2
x3010 | 1 1 1 1 0 0 0 0 0 0 1 0 0 0 0 1 | Print R0 (TRAP x21)
x3011 | 1 1 1 1 0 0 0 0 0 0 1 0 0 1 0 1 | HALT (TRAP x25)
X3012 | 0 0 0 0 0 0 0 0 0 0 1 1 0 0 0 0 | ASCII x30 (‘0’)

## Slide 42: LC-3 Data Path Revisited
Filled arrow
= info to be processed.
Unfilled arrow = control signal.

## Slide 43: Data Path Components
Global bus
  special set of wires that carry a 16-bit signal to many components
  inputs to the bus are “tri-state devices,” that only place a signal on the bus when they are enabled
  only one (16-bit) signal should be enabled at any time
    control unit decides which signal “drives” the bus
  any number of components can read the bus
    register only captures bus data if it is write-enabled by the control unit
Memory
  Control and data registers for memory and I/O devices
  memory: MAR, MDR (also control signal for read/write)

## Slide 44: Data Path Components
ALU
  Accepts inputs from register file and from sign-extended bits from IR (immediate field).
  Output goes to bus.
    used by condition code logic, register file, memory
Register File
  Two read addresses (SR1, SR2), one write address (DR)
  Input from bus
    result of ALU operation or memory read
  Two 16-bit outputs
    used by ALU, PC, memory address
    data for store instructions passes through ALU

## Slide 45: Data Path Components
More details later.
Multiplexer (MUX): selects data from multiple sources
PC and PCMUX
  Three inputs to PC, controlled by PCMUX
    PC+1 – FETCH stage
    Address adder – BR, JMP
    bus – TRAP (discussed later)
MAR and MARMUX
  Two inputs to MAR, controlled by MARMUX
    Address adder – LD/ST, LDR/STR
    Zero-extended IR[7:0] -- TRAP (discussed later)

## Slide 46: Data Path Components
Condition Code Logic
  Looks at value on bus and generates N, Z, P signals
  Registers set only when control unit enables them (LD.CC)
    only certain instructions set the codes (ADD, AND, NOT, LD, LDI, LDR, LEA)
Control Unit – Finite State Machine
  On each machine cycle, changes control signals for next phase of instruction processing
    who drives the bus? (GatePC, GateALU, …)
    which registers are write enabled? (LD.IR, LD.REG, …)
    which operation should ALU perform? (ALUK)
    …
  Logic includes decoder for opcode, etc.