## Slide 1: Chapter 6 Programming Most of the material is left for your to study yourself.

## Slide 2: Solving Complex Problems - Less coding more writing
Problem Solving
  How do we figure out what to tell the computer to do?
    Convert problem statement into algorithm, using stepwise refinement.
    Convert algorithm into LC-3 machine instructions.
Debugging
  How do we figure out why it didn’t work?
  Examining registers and memory, setting breakpoints, etc.
Time spent on the first reduces time spent on the second!

## Slide 3: Stepwise Refinement
Also known as systematic decomposition.
Start with problem statement:
  “We wish to count the number of occurrences of a character in a file. The character in question is to be input from the keyboard; the result is to be displayed on the monitor.”
Decompose task into a few simpler subtasks.
Decompose each subtask into smaller subtasks, and these into even smaller subtasks, etc., until you get to the machine instruction level.

## Slide 4: Problem Statement
Because problem statements are written in English, they are sometimes ambiguous and/or incomplete.
  Where is “file” located? How big is it, or how do I know when I’ve reached the end?
  How should final count be printed? A decimal number?
  If the character is a letter, should I count both upper-case and lower-case occurrences?
How do you resolve these issues?
  First make sure you have fully understood the existing specifications, then
  Ask the person who wants the problem solved, or
  Make a decision and document it.

## Slide 5: Three Basic Constructs
There are three basic ways to decompose a task:

## Slide 6: Sequential
Do Subtask 1 to completion, then do Subtask 2 to completion, etc.

## Slide 7: Conditional
If condition is true, do Subtask 1; else, do Subtask 2.

## Slide 8: Iterative
Do Subtask over and over, as long as the test condition is true.

## Slide 9: Problem Solving Skills
Learn to convert problem statement into step-by-step description of subtasks.
  Like a puzzle, or a “word problem” from grade school math.
    What is the starting state of the system?
    What is the desired ending state?
    How do we move from one state to another?
  Recognize English words that correlate to three basic constructs:
    “do A then do B”  sequential
    “if G, then do H”  conditional
    “for each X, do Y”  iterative
    “do Z until W”  iterative

## Slide 10: LC-3 Control Instructions
How do we use LC-3 instructions to encode the three basic constructs?
Sequential
  Instructions naturally flow from one to the next, so no special instructions needed to go from one sequential subtask to the next.
    Von Neumann architecture
Conditional and Iterative
  Create code that converts condition into N, Z, or P. Example: Condition: “Does R0 = R1?” Code: Subtract R1 from R0; if equal, Z bit will be set.
  Then use BR instruction to transfer control to the proper subtask.

## Slide 11: Code for Conditional
Exact bits depend
on condition
being tested
PC offset to address C
PC offset to address D
Unconditional branch to Next Subtask
Assuming all addresses are close enough that PC-relative branch can be used.

## Slide 12: Code for Iteration
Exact bits depend
on condition
being tested
PC offset to
address C
PC offset to address A
Unconditional branch to retest condition

## Slide 13: Example: Counting Characters
Initial refinement: Big task into three sequential subtasks.

## Slide 14: Refining B
Refining B into iterative construct.

## Slide 15: Refining B1
Refining B1 into sequential subtasks.

## Slide 16: Refining B2 and B3
Conditional (B2) and sequential (B3). Use of LC-2 registers and instructions.

## Slide 17: The Last Step: LC-3 Instructions
Use comments to separate into modules and to document your code.
;
; Test character for end of file
;
TEST ADD R4, R1, #-4 ; Test for EOT (ASCII x04)
BRz OUTPUT ; If done, prepare the output
;
; Test character for match. If a match, increment count.
;
NOT R1, R1
ADD R1, R1, R0 ; If match, R1 = xFFFF
NOT R1, R1 ; If match, R1 = x0000
BRnp GETCHAR ;
ADD R2, R2, #1
;
; Get next character from file.
;
GETCHAR ADD R3, R3, #1 ; Point to next ch
LDR R1, R3, #0 ; R1 gets next char
BRnzp TEST
This level of detail may not seam necessary with simple programs, but in industry thousands to millions of lines of code per program is common, with no additional documentation

## Slide 18: Debugging
You’ve written your program and it doesn’t work.
Now what?
What do you do when you’re lost in a city?
  Drive around randomly and hope you find it?
  Return to a known point and look at a map?
In debugging, the equivalent to looking at a map is tracing your program.
  Examine the sequence of instructions being executed.
  Keep track of results being produced.
  Compare result from each instruction to the expected result.

## Slide 19: Definitions
Breakpoint: location in code where execution will pause, set in LC3 by a double click
Continue: execute program until it completes normally or hits a breakpoint
Finish: execute program until the current function returns or breakpoint is hit
Step: execute code until next line of source code (one instruction in the LC3)
  Next line of code may be in another function
Next: execute code until next line of source code in the current function
  Does not enter function calls

## Slide 20: Debugging
Will be skipped in the class.
The examples assumes that the programs are given only in binary.

## Slide 21: Debugging Operations
Any debugging environment should provide means to:
  Display values in memory and registers.
  Deposit values in memory and registers.
  Execute instruction sequence in a program.
  Stop execution when desired.
Different programming levels offer different tools.
  High-level languages (C, Java, ...) usually have source-code debugging tools.
  For debugging at the machine instruction level:
    simulators
    operating system “monitor” tools
    in-circuit emulators (ICE)
      plug-in hardware replacements that give instruction-level control

## Slide 22: LC-3 Simulator
set/display
registers
and memory
execute
instruction
sequences
stop execution,
set breakpoints

## Slide 23: Types of Errors
Syntax Errors
  You made a typing error that resulted in an illegal operation.
  Not usually an issue with machine language, because almost any bit pattern corresponds to some legal instruction.
  In high-level languages, these are often caught during the translation from language to machine code.
Logic Errors
  Your program is legal, but wrong, so the results don’t match the problem statement.
  Trace the program to see what’s really happening and determine how to get the proper behavior.
Data Errors
  Input data is different than what you expected.
  Test the program with a wide variety of inputs.

## Slide 24: Tracing the Program
Execute the program one piece at a time, examining register and memory to see results at each step.
Single-Stepping
  Execute one instruction at a time.
  Tedious, but useful to help you verify each step of your program.
Breakpoints
  Tell the simulator to stop executing when it reaches a specific instruction.
  Check overall results at specific points in the program.
    Lets you quickly execute sequences to get a high-level overview of the execution behavior.
    Quickly execute sequences that your believe are correct.
Watchpoints
  Tell the simulator to stop when a register or memory location changes or when it equals a specific value.
  Useful when you don’t know where or when a value is changed.

## Slide 25: Example 1: Multiply
This program is supposed to multiply the two unsigned integers in R4 and R5.
x3200 0101010010100000
x3201 0001010010000100
x3202 0001101101111111
x3203 0000011111111101
x3204 1111000000100101
clear R2
add R4 to R2
decrement R5
R5 = 0?
HALT
No
Yes
Set R4 = 10, R5 =3.
Run program.
Result: R2 = 40, not 30.

## Slide 26: Debugging the Multiply Program
PC | R2 | R4 | R5
x3200 | -- | 10 | 3
x3201 | 0 | 10 | 3
x3202 | 10 | 10 | 3
x3203 | 10 | 10 | 2
x3201 | 10 | 10 | 2
x3202 | 20 | 10 | 2
x3203 | 20 | 10 | 1
x3201 | 20 | 10 | 1
x3202 | 30 | 10 | 1
x3203 | 30 | 10 | 0
x3201 | 30 | 10 | 0
x3202 | 40 | 10 | 0
x3203 | 40 | 10 | -1
x3204 | 40 | 10 | -1
 | 40 | 10 | -1
PC and registers
at the beginning
of each instruction
PC | R2 | R4 | R5
x3203 | 10 | 10 | 2
x3203 | 20 | 10 | 1
x3203 | 30 | 10 | 0
x3203 | 40 | 10 | -1
 | 40 | 10 | -1
Single-stepping
Breakpoint at branch (x3203)
Executing loop one time too many.
Branch at x3203 should be based on Z bit only, not Z and P.
Should stop looping here!

## Slide 27: Example 2: Summing an Array of Numbers
This program is supposed to sum the numbers stored in 10 locations beginning with x3100, leaving the result in R1.
R4 = 0?
HALT
No
Yes
R1 = 0 R4 = 10
R2 = x3100
R1 = R1 + M[R2]
R2 = R2 + 1
R4 = R4 - 1
x3000 0101001001100000
x3001 0101100100100000
x3002 0001100100101010
x3003 0010010011111100
x3004 0110011010000000
x3005 0001010010100001
x3006 0001001001000011
x3007 0001100100111111
x3008 0000001111111011
x3009 1111000000100101

## Slide 28: Debugging the Summing Program
Running the the data below yields R1 = x0024, but the sum should be x8135. What happened?
Address | Contents
x3100 | x3107
x3101 | x2819
x3102 | x0110
x3103 | x0310
x3104 | x0110
x3105 | x1110
x3106 | x11B1
x3107 | x0019
x3108 | x0007
x3109 | x0004
PC | R1 | R2 | R4
x3000 | -- | -- | --
x3001 | 0 | -- | --
x3002 | 0 | -- | 0
x3003 | 0 | -- | 10
x3004 | 0 | x3107 | 10
Start single-stepping program...
Should be x3100!
Loading contents of M[x3100], not address.
Change opcode of x3003 from 0010 (LD) to 1110 (LEA).

## Slide 29: Example 3: Looking for a 5
This program is supposed to set R0=1, if there’s a 5 in one ten memory locations, starting at x3100. Else, it should set R0 to 0.
R2 = 5?
HALT
No
Yes
R0 = 1, R1 = -5, R3 = 10 R4 = x3100, R2 = M[R4]
R4 = R4 + 1
R3 = R3-1
R2 = M[R4]
x3000 0101000000100000
x3001 0001000000100001
x3002 0101001001100000
x3003 0001001001111011
x3004 0101011011100000
x3005 0001011011101010
x3006 0010100000001001
x3007 0110010100000000
x3008 0001010010000001
x3009 0000010000000101
x300A 0001100100100001
x300B 0001011011111111
x300C 0110010100000000
x300D 0000001111111010
x300E 0101000000100000
x300F 1111000000100101
x3010 0011000100000000
R3 = 0?
R0 = 0
Yes
No

## Slide 30: Debugging the Fives Program
Running the program with a 5 in location x3108 results in R0 = 0, not R0 = 1. What happened?
Address | Contents
x3100 | 9
x3101 | 7
x3102 | 32
x3103 | 0
x3104 | -8
x3105 | 19
x3106 | 6
x3107 | 13
x3108 | 5
x3109 | 61
Perhaps we didn’t look at all the data? Put a breakpoint at x300D to see how many times we branch back.
PC | R0 | R2 | R3 | R4
x300D | 1 | 7 | 9 | x3101
x300D | 1 | 32 | 8 | x3102
x300D | 1 | 0 | 7 | x3103
 | 0 | 0 | 7 | x3103
Didn’t branch back, even though R3 > 0?
Branch uses condition code set by loading R2 with M[R4], not by decrementing R3.
Swap x300B and x300C, or remove x300C and branch back to x3007.

## Slide 31: Example 4: Finding First 1 in a Word
This program is supposed to return (in R1) the bit position of the first 1 in a word. The address of the word is in location x3009 (just past the end of the program). If there are no ones, R1 should be set to –1.
R1 = 15
R2 = data
R2[15] = 1?
decrement R1
shift R2 left one bit
HALT
x3000 0101001001100000
x3001 0001001001101111
x3002 1010010000000110
x3003 0000100000000100
x3004 0001001001111111
x3005 0001010010000010
x3006 0000100000000001
x3007 0000111111111100
x3008 1111000000100101
x3009 0011000100000000
R2[15] = 1?
Yes
Yes
No
No

## Slide 32: Debugging the First-One Program
Program works most of the time, but if data is zero, it never seems to HALT.
PC | R1
x3007 | 14
x3007 | 13
x3007 | 12
x3007 | 11
x3007 | 10
x3007 | 9
x3007 | 8
x3007 | 7
x3007 | 6
x3007 | 5
Breakpoint at backwards branch (x3007)
PC | R1
x3007 | 4
x3007 | 3
x3007 | 2
x3007 | 1
x3007 | 0
x3007 | -1
x3007 | -2
x3007 | -3
x3007 | -4
x3007 | -5
If no ones, then branch to HALT never occurs!
This is called an “infinite loop.”
Must change algorithm to either (a) check for special case (R2=0), or (b) exit loop if R1 < 0.

## Slide 33: Debugging: Lessons Learned
Trace program to see what’s going on.
  Breakpoints, single-stepping
When tracing, make sure to notice what’s really happening, not what you think should happen.
  In summing program, it would be easy to not notice that address x3107 was loaded instead of x3100.
Test your program using a variety of input data.
  In Examples 3 and 4, the program works for many data sets.
  Be sure to test extreme cases (all ones, no ones, ...).